## Slide 1: ATLAHS: An Application-centric Network Simulator Toolchain for AI, HPC and Distributed Storage
Siyuan Shen1*, Tommaso Bonato1*, Zhiyi Hu1, Pasquale Jordan1, Tiancheng Chen1, Torsten Hoefler1
1 ETH Zurich, * Equal contribution

## Slide 2: Importance of Real Application Traces: An Example
Comp
DP
PP
Streams
Node 0
Node 8
Comp
DP
PP
Streams
Partition 0
Partition 1
Time
BWD
Allreduce
Allreduce
Receive
BWD
Send
Pipeline parallelism (PP) affected by long running allreduce
Layer
Layer
Backpropagation
Node 0
Node 8
Node 1
Node 9
Node 2
Node 10
Node 7
Node 15
Forward
Forward
Forward
Forward
Backward
Backward
Backward
Backward
Input
Input
Input
Input
Loss
Loss
Loss
Loss
Implemented with point-to-point operations (i.e., send, receive)
Gradient synchronization is done with Allreduce
Pipeline Parallelism (PP = 2)
Data Parallelism (DP = 8)
N0
N1
N2
N3
N8
N9
N10
N11
DP Ring Allreduce
PP Victim Flow
Ring allreduce for data parallelism (DP)
Notes: --llama

## Slide 3: Importance of Real Application Traces: An Example
Comp
DP
PP
Streams
Node 0
Node 8
Comp
DP
PP
Streams
Partition 0
Partition 1
Time
BWD
Allreduce
Allreduce
Receive
BWD
Send
Pipeline parallelism (PP) affected by long running allreduce
Layer
Layer
Backpropagation
Node 0
Node 8
Node 1
Node 9
Node 2
Node 10
Node 7
Node 15
Forward
Forward
Forward
Forward
Backward
Backward
Backward
Backward
Input
Input
Input
Input
Loss
Loss
Loss
Loss
Implemented with point-to-point operations (i.e., send, receive)
Gradient synchronization is done with Allreduce
Pipeline Parallelism (PP = 2)
Data Parallelism (DP = 8)
N0
N1
N2
N3
N8
N9
N10
N11
DP Ring Allreduce
PP Victim Flow
Ring allreduce for data parallelism (DP)
x
We need an application-centric approach for generating workloads for network simulators

## Slide 4: Why Another Simulator?
Requirements
Support real applications from various domains (e.g., HPC, AI, distributed storage, etc.)
Allow all types of workloads to be stored and executed in a standardized trace format (not ad-hoc)
Simulator Toolchains
LogGOPSim [1]
CODES [3]
AstraSim [5]
SimAI [7]
HPC
The trace format and the toolchain need to be flexible and extensible
[1] Hoefler et al. (2010). LogGOPSim: simulating large-scale applications in the LogGOPS model. HPDC
HPC
AI
AI
GOAL [2]
OTF [4]
Chakra [6]
[3] Jain et al. (2016). Evaluating HPC Networks via Simulation of Parallel Workloads. SC
[7] Wang et al. (2025). SimAI: Unifying Architecture Design and Performance Tuning for Large-Scale Large Language Model Training with Scalability and Precision. NSDI
[5] Won et al. (2023). ASTRA-sim2.0: Modeling Hierarchical Networks and Disaggregated Systems for Large-model Training at Scale. ISPASS
[2] Hoefler et al. (2009). Group operation assembly language - a flexible way to express collective communication. International Conference on Parallel Processing
[4] Knüpfer et al. (2006). Introducing the Open Trace Format (OTF). In Lecture notes in computer science
[6] Sridharan et al. (2023). Chakra: Advancing Performance Benchmarking and Co-design using Standardized Execution Traces. arXiv
Notes: Fully open source?
Compressed

## Slide 5: ATLAHS Toolchain
GOAL Format
Configuration
Network Topology
Latency
...
Bandwidth
CC Algorithm
MTU
Workload Simulation
Scheduler
Network Backend
LogGOPSim
...
NS3
htsim
Input Parameters
Number of Ranks
Collective Algorithm
...
Synthetic Workloads
Applications
HPC
Node
Application
P2P, Collectives
...
MPI
PMPI
Tracer
Storage
Example: Azure Direct Drive
Coordinator
Block Storage
Metadata
Load Balancer
Gateway
Node
Virtual Disk Client
Application
Read
Write
Block I/O Tracer
Trace Files
I/O
MPI
NCCL
AI
Stream 0
Allreduce
Send
Stream 1
Broadcast
Recv
Inter-node and intra-node sends and receives
Collective Algorithm
Node
GPU 0
GPU 1
...
NCCL
Tracer
Custom tracers and parsers can be added to support more applications
Red: Application and hardware components
Green: Trace processing
Blue: Simulation
ATLAHS: Application-centric Network Simulator Toolchain for AI, HPC, and Distributed Storage
Notes: Grey parameters

## Slide 6: Group Operation Assembly Language (GOAL): A Unifying Trace Format
Compute Stream 1
Compute Stream 0
rank 0 {
l1: calc 100
l2: calc 200
l3: calc 200
l2 requires l1
l3 requires l1
l4: send 10b to 1
l4 requires l2
l4 requires l3
}
calc 100
calc 200
calc 200
send 10b
Directed Acyclic Graph (DAG)
Vertices represent tasks:
Send
Receive
Computation
Edges define dependencies between tasks
cpu 0
cpu 1
Tasks can be assigned to different hardware resources by using cpu and nic labels
Textual Format
DAG Schedule
Stored and executed in binary format: light-weight, storage space efficient
Simple and intuitive structure: easy to adapt and extend

## Slide 7: Workload Generation: HPC
MPI_Init(NULL, NULL);
MPI_Comm_size(MPI_COMM_WORLD, &size); MPI_Irecv(&received, 1, MPI_INT, SENDER, 0,
MPI_COMM_WORLD, &request);
MPI Program
MPI Trace
MPI_Init:0:0
MPI_Comm_size:7:0:256:8
MPI_Irecv:1547003:0:3500:15:1:1:5:6:1547032
Start time
Other arguments
End time
GOAL Schedule
Program traced with liballprof [1] relying on the PMPI interface
[1] Hoefler et al. (2010). LogGOPSim: simulating large-scale applications in the LogGOPS model. HPDC
GOAL generated with Schedgen [1]
Computation inferred from timestamps between consecutive MPI operations
Collectives decomposed into individual sends and receives

## Slide 8: Workload Generation: AI
Node 0
AI App
NCCL
GPU 0
GPU 1
NCCL with additional nvtx annotations
Node 1
GPU 2
GPU 3
STAGE 2
STAGE 3
Nsys Report Files
...
GPU 1
Stream 0
Bcast
Send
Stream 1
Allreduce
GPU 0
Stream DAGs
...
GPU 0
GPU 1
Stream 0
Stream 1
Allreduce
Send
Bcast
Dummy
Dummy
STAGE 4
GOAL
GPU 0
GPU 1
Node 0
GPU 2
GPU 3
Node 1
nsys profile
STAGE 1
Collective Decomposition DAGs
Collectives are replaced with point-to-point algorithms
GPU 0
GPU 1
GPU 2
GPU 3
Stream 1
Stream 0
Ops from different CUDA streams are assigned different compute streams in GOAL

## Slide 9: Decomposition for NCCL Collectives
Node 0
GPU 0
SM
SM
SM
SM
GPU 1
Node 1
GPU 2
GPU 3
NCCL uses
1 SM
Timeline
NCCL Ring Broadcast (2MB)
Send to GPU2 (0.5MB)
Send to GPU2 (0.5MB)
Send to GPU2 (0.5MB)
Send to GPU2 (0.5MB)
Implementation of NCCL collectives depends on
Algorithm: Ring, Tree, NVLS, CollNet, etc.
Communication Protocol: Simple, LL, LL128
Number of NCCL channels
Converting NCCL collectives into GOAL is complex
NCCL’s Iterative execution model

## Slide 10: Workload Generation: Distributed Storage System
Node
CCSi
BSSj
Example System: Azure Direct Drive
...
...
CCS0
CCS1
CCSN
MDS
GS
SLB
BSS0
BSS1
BSSM
Node
Application
Read
Write
Virtual Disk Client (VDC)
Traced with bpftrace
Stored in SPC format
CCS: Change Coordinate Service
BSS: Block Storage Service
MDS: Metadata Service
GS: Gateway Service
SLB: Software Load Balancer
Read Request

## Slide 11: Integration with Network Simulator
Workload Simulation Pipeline
GOAL File
Configuration
Topology
...
Bandwidth
Latency
The core interfaces provide a unified method for simulation setup and event handling.
ATLAHS Entry Point
GOAL Scheduler
ATLAHS API
send
recv
calc
Network Backend
LGS
htsim
NS3
...
Send
Recv
Calc
class ATLAHS_API {
virtual void simulationSetup();
virtual void eventOver(Event);
virtual void send(SendEvent);
virtual void recv(RecvEvent);
virtual void calc(CalcEvent);
};
...
Requirements
Few well-defined APIs that any network simulator can use to integrate into its logic.
Provide users with flexibility depending on their needs (message-level vs packet-level)
Low overhead compared to running the simulator on its own.
Packet-Level Simulators
Slow and high memory requirement
Good approximation and can test more things
Low accuracy in some cases
Fast and good approximation in many cases
Message-Level Simulators

## Slide 12: Validation: AI
Grace Hopper Superchips (GH200)
150 GB/s intra-node communication
25 GB/s Cray Slingshot
Dragonfly topology
Alps Supercomputer (CSCS)
TP: Tensor parallelism
PP: Pipeline parallelism
DP: Data parallelism
EP: Expert parallelism
AstraSim only executed successfully for two configurations, encountering runtime errors in all other scenarios
ATLAHS LogGOPSim backend runs on average faster than AstraSim’s analytical backend
Notes: Clarify 8x

## Slide 13: Validation: HPC
Intel Xeon E5-2660 v2 CPU
32 GB DDR3 RAM, ConnectX-3 NIC
Fat Tree topology (18 Mellanox SX6036 switches)
188-node Testbed (CSCS)

## Slide 14: Use Cases of ATLAHS
We validated ATLAHS accuracy, but what can it practically be used for?
Estimate runtimes with different network configurations
Study and analyze traffic patterns and bottlenecks
Compare different congestion control algorithms
Study the effect of jobs placement
Determine the effect of using different collectives
Determine the impact of network failures on a variety of workloads

## Slide 15: Case Study: Effect of CC on Distributed Storage Requests
Topologies
400 Gbps network with two different Fat Tree topologies
Comparing MPRDMA and NDP congestion control algorithms
5k storage requests
htsim simulator setup
With oversubscription, NDP, a receiver-based congestion control, struggles to see in-network congestion.
With no oversubscription both Congestion Control algorithms have comparable performance.
Non-Oversubscribed
Oversubscribed
MPRDMA
  Sender-based
  Can deal with congetion anywhere in the network
NDP
  Receiver-based
  Fair and perfect incast performance
Congestion Control Algorithms

## Slide 16: Case Study: ATLAHS LGS vs ATLAHS htsim
400 Gbps network with two different Fat Tree topologies w
Comparing ATLAHS LGS and ATLAHS htsim
Running Llama 7B
Simulation Setup
If ATLAHS LGS is usually matching ATLAHS htsim, why bother running slow packet-level simulators?
ATLAHS LGS assumes a fully connected topology
ATLAHS LGS assumes no failures or asymmetries
ATLAHS LGS assumes no queue build up or congestion handling
ATLAHS LGS does not model reliability or load balancing
With ATLAHS htsim we can also access more metrics such as packet drops and many more

## Slide 17: ATLAHS Trace Dataset
We opensource ATLAHS along with all traces collected this work
(unprocessed trace files + GOAL)
The dataset is still growing!
Realistic application are critical but also rare for accurate network simulation

## Slide 18: Conclusions
More of SPCL’s research:
… or spcl.ethz.ch
180+ Talks
youtube.com/@spcl
twitter.com/spcl_eth
1.4K+ Followers
github.com/spcl
3.8K+ Stars
https://github.com/spcl/atlahs
Many more results in the paper:
https://arxiv.org/pdf/2505.08936